## Slide 1
Per- and Polyfluoroalkyl Substances
Background Information
Janet Anderson, Ph.D., DABT
Integral Consulting, Inc.
April 16, 2019 – NASF Washington Forum

## Slide 2: Per- and Polyfluoroalkyl Substances (PFAS)

## Slide 3: Family Tree of PFAS
Red = Restricted
Examples of
Individual compounds
Number of peer-reviewed articles since 2002
Wang et al. (2017)
Complicated nomenclature and chemistries
>4,000 may have been on, or associated with, the on global market
Notes: Add nomenclature complicated and move >3000 comment

## Slide 4: PFAS Chemistry and Nomenclature
PFAS = Per- and Polyfluoroalkyl substances
  Two or more carbons joined, plus multiple fluorines
Perfluoroalkyl acids
  “Per” = fully fluorinated
  e.g., PFOS and PFOA
Polyfluoroalkyl substance
  “Poly” = many fluorines
  e.g., 6:2 FTS
  Fluorotelomer sulfonate
Polymers (e.g., PTFE)
Non-Polymers
polyfluoro
PFAA
perfluoro

## Slide 5: PFAS: Chemical Properties
Heat resistant
Stain resistant
Resistant to biodegradation
High water solubility
C-F strongest bond in nature
Highly sorbent
High surface tension

## Slide 6: Why the Concern?
Anthropogenic chemicals with widespread use since the 1940s
Evolving science
Some may be regarded as
  Persistent
  Bioacuumulative
  Toxic
Some appear to be ubiquitous at low levels
PFOA
  Arkema, Asahi, BASF Corporation, Clariant, Daikin, 3M/Dyneon, DuPont, Solvay Solexis
  Voluntarily discontinued ≤2015
PFOS
  3M
  Voluntarily discontinued in 2002

## Slide 7: Wide-Spread Environmental Occurrence
Some PFAS ubiquitous at low concentrations
High-concentration are typically found near
  Manufacturing facilities
  Military and civilian airports, refineries, and other locations with fuel fires or fuel fire training sites
  Textile mills
  Wastewater treatment plant (WWTP) outfalls
  Biosolids application areas
Image?
Oliaei et al. (2013), Environ Sci Pollut Res

## Slide 8: How did we get here?
2006
EPA “PFOA Stewardship Program”
1/2006
1940-50s
2009
2009
TSCA “Long-Chain PFC Action Plan”
2013
2016
UCMR3
Testing
2018
5/2018
3M Phase-out of PFOS
2000-2002
12/2009
1969
2013–2015
EPA Provisional Health Advisories for DW
DuPont, WV; Leach Settlement
C8 Health Studies Begin
2004
1/2018
3M NRDA $850M Settlement
EPA Lifetime
Health Advisories
5/2016
AFFF
PFAS U.S. Timeline of Key Events
1979
PFAS Chemical Engineering
TSCA Chemical Substance Inventory
1970s
2019
EPA PFAS Action Plan
2/2019
EPA PFAS Leadership Summit
2/2017
DuPont Class Action Settlement ($671M)
Widespread use in industry
Switch to “replacement chemistry”
Litigation, regulatory attention, ongoing research
Notes: Note the Animation on this slide

## Slide 9
Per- and Polyfluoroalkyl Substances
Metal Plating and Surface Coating Perspective
Janet Anderson, Ph.D., DABT
Integral Consulting, Inc.
April 16, 2019 – NASF Washington Forum

## Slide 10: PFAS are Essential in Chrome Plating, Etching
Increases quality of plating baths, reduces waste
Results in high corrosion resistance
Wetting and leveling to improve etching process
Improves worker and environmental safety (e.g., hexavalent chrome)
  Suppresses hexavalent chromium vapors by reducing surface tension of solution
  CAA MACT Cr(VI) limits
  OSHA worker safety requirements

## Slide 11: Key PFAS U.S. Milestones for NASF
2007
MN identified metal plating shops as source of PFOS in environment
2007
1940-50s
2009
2009
2012-15
2016
Phase-out of PFOS-based mist suppressants under NESHAP
2018
5/2018
3M Phase-out of PFOS
2000-2002
1954
2012–2015
USEPA Reg 5 PFOS Chromium Electroplating Study
2018
Industry mtgs with stakeholders (e.g. DoD, EPA Reg 5)
EPA Lifetime
Health Advisories
5/2016
PFAS used in chromium plating
PFAS U.S. Timeline of Key Events
PFAS Chemical Engineering
2019
EPA PFAS Action Plan
2/2019
EPA PFAS Leadership Summit
Notes: Animation

## Slide 12: Industry-EPA Collaboration to Ban PFOS in Chromium Plating Switch from PFOS (historic) to 6:2 FTS (current, U.S.)
Perfluorooctane sulfonate
6:2 Fluoroteolomer sulfonate
PTFE

## Slide 13: Then Why Do We Still Care?
Legacy Environmental Liability
Replacements, Product Stewardship, Best Practices

## Slide 14: Interest in PFAS in Industry Effluent Discharge is Increasing
EPA - study of PFAS in industry discharge (see EPA’s Final 2016 Effluent Guidelines Program Plan, April 2018)
Important discussion topic at the state level
  Minnesota - state-wide testing of WWTP effluent in 2007 (identified local chromium electroplating facility as contributor of PFOS to WWTP)
  Michigan - promulgated PFOS surface water quality standard of 12 ppt

## Slide 15
Increasing Scrutiny on ALL PFAS and Metal Plating
Legacy Uses, Environmental Liability
Replacements, Product Stewardship, Best Practices
Bipartisan Bill Introduced (March ‘19)
“PFAS Detection Act of 2019”

## Slide 16: Transition to Short Fluorotelomers Improves Risk Profile
Non-PFAS formulations aren’t effective hexavalent chromium mist suppressants
Generally accepted that fluorotelomers are:
  Less persistent
  Less bioaccumulative
  Less toxic
Data gaps remain
PFOS
6:2 FTS
Notes: Discuss 6:2FTS performance compared to PFOS

## Slide 17: Available Data to Support the Transition to 6:2 FTS – Data gaps Remain
Supporting Data
Data Gaps
Lower human exposure to 6:2 FTS compared to PFOS
PFOS is persistent; 6:2 FTS can biodegrade
6:2 FTS is not considered bioaccumulative
6:2 FTS is less toxic than PFOS to some organisms
Few studies have monitored human exposure to 6:2 FTS
Degradation products not fully characterized
Bioaccumulation of 6:2 FTS in humans is not characterized
No long term studies and toxicity of 6:2 FTS to humans is unknown

## Slide 18: What is NASF/Policy Group Doing?
NASF PFAS Technical Working Group
Identifying and securing experts and resources
Meeting with stakeholders to understand landscape
Helping to prioritize actions
PFOS
6:2 FTS

## Slide 19: NASF Identified 4 Priority Issues
Why is there still residual PFOS in chrome plating shop effluent today?
What is in current PFAS formulations and what data supports its continued use?
What contribution do plating shops have to the overall load of PFAS into POTWs/WWTPs?
How to best engage and educate key stakeholders?

## Slide 20: Metal Plating Shop Effluent is Only One Contributor of PFAS to POTWs

## Slide 21: Key Take Home Messages
Intense state and community focus on PFAS
  Disparate regulatory actions, public mistrust, and increasing litigation
Increasing scrutiny on metal plating industry as an environmental source
NASF/Policy Group has been, and will continue to be, engaged and actively promoting
  sound science-based regulations, and
  best industry practices

## Slide 22
Janet Anderson, Ph.D., DABT
Toxicologist | Senior Consultant
janderson@integral-corp.com
513.226.6528
Questions?

## Slide 23: Understand Detections of PFOS in Facility Effluent
EPA Region 5 (Michigan)
Ensure sound science and logic drive sampling program and data interpretation
Collaborate with regulators & other stakeholders
Source: EPA 1998. Characterizing Risk at Metal Finishing Facilities

## Slide 24: Mist Suppressant Formulations Still Contain PFAS, but Exact Formulations are Confidential
Collaborate with industry suppliers and regulators
Ensure a data-driven analytical plan that protects CBI and helps resolve questions
  Active ingredients
  Impurities
Notes: Image of mist suppressant bottle/drum

## Slide 25: Back-up Slides

## Slide 26: PFOA/PFOS Human Data Challenging to Interpret
Overall weight of evidence has NOT identified a strong association between exposure to a specific PFAS and any adverse health outcome
EPA and ATSDR: Most consistent evidence generally exists for associations with:
↑ Cholesterol, liver enzymes
↓ Antibody response to vaccine
Pregnancy-induced hypertension/pre-eclampsia
Risk of thyroid disease
↓ Fertility
↓ Birth weight
AUS DOH: Limited or no evidence for any causal link and any human disease
Associations with some health outcomes but
Limited or no evidence of human disease
Lack of clinical significance
May be explained by reverse causation or confounding factors
Notes: animation

## Slide 27: Regulatory Numbers Based on Animal Data: Many Issues and Uncertainties…
Developmental
Immune
Liver
Thyroid
Liver
Cholesterol
  (not persistent)
Policy and precautionary principal
?
Notes: USEPA chose developmental endpoints from rodents – bone ossification, changes in puberty markers (PFOA), and decreased neonatal body weight (PFOS)

## Slide 28: States – Leading the Charge, Not Just for Drinking Water Standards and Exposure
Increasing list of analytes
Increasingly divergent priorities
Increased attention to non-AFFF sources
  Landfills
  POTWs
Additional exposure routes
  Surface water
  Effluent
  Soil
  Food
Increasing use of state legislature
  >80 Legislative bills related to PFAS issued in FY18

## Slide 29: USEPA 2019 - PFAS Action Plan
Regulation (PFOA, PFOS)
CERCLA - hazardous substance listing
Toxicology
Collaboration w/industry, academia
Monitoring and Remediation
Public water supplies - expand monitoring via UCMR4
Risk Communication
Risk communication toolbox
SDWA - MCLs proposed in 2019
Interim cleanup levels
Continue research on additional PFAS
Consistency messaging across agencies
Develop new treatment technologies
TSCA - additional SNURs
Air emissions - reporting via Toxic Release Inventory
Explore AWQCs and Effluent limits

## Slide 30: What Is Your PFAS Analyte List?
USEPA Method 537.1
  12 PFAAs
  2 precursors
  4 new – (GenX, ADONA, F-53B)
  18 total
Commercial labs
  ~30-44 analytes
Academia
  ~400 analytes

## Slide 31: Total Oxidizable Precursor Assay
Source: TestAmerica: Closing the PFAS Mass Balance
White Paper No. CA-T-W-006, rev 1 - July, 2017
Is NOT a predictor of abiotic and biotic breakdown in environment
Useful for remedial design to account for loading, etc.
Not useful for risk assessment.